RALLS COUNTY HEALTH DEPARTMENT

PROCEDURES TO OBTAIN A PERMIT

FOR AN ON-SITE WASTEWATERTREATMENT SYSTEM

Please Note: A PERMIT is required for all new systems, regardless of lot size, and for repair, replacement or upgrade of an existing system (includes a septic tank, lateral, holding tank, etc.)

The Installer must ensure that a permit has been issued prior to beginning construction.

Notify the Ralls County Health Department between forty-eight (48) and four (4) hours prior to beginning installation of the system.  Unless rain is imminent, do not backfill a system until it is inspected or authorization is received from the Ralls County Health Department.

- Obtain an “Application Form for An On-Site Wastewater System Construction Permit” from the Ralls County Health Department.

- Contact a Registered Soil Scientist and request a soil morphology or “Soil Test”.  A list of Dept. of Health & Senior Services (DHSS) Registered Soil Scientists will be provided by the Health Department.

- Select a Registered Installer from the list provided by the Health Department.  All installers must register each year with the Ralls County Health Department before beginning work on an on-site system, regardless of other registration or certification (installers are also required by state law to be registered with DHSS).

- Complete the Application Form, using the information from the Soil Scientist’s report.  The application must include a sketch showing the proposed layout of the components of the system (with lengths of pipes and separation distances indicated), and showing property lines, structures, water lines, wells, house location, etc., with setback distances indicated for each of these. (see footnote #2).

- Submit the Completed Application Form with your Signature and the signature of your installer to the Ralls County Health Department for review and approval.  Note: The application form is not a Permit- see a reduced size sample of a Permit on the other side of this page, and see footnote (*1)

- The Permit Fee is $115.00-checks are payable to the Ralls County Health Department.  Upon receipt of the fee (if required) and approval of the Application, a “Ralls County On-Site Wastewater Treatment System Construction Permit” will be issued.  Construction of the system may not begin until the Permit has been issued.  The Installer must ensure that a Permit has been issued prior to beginning construction.  This includes setting a septic tank or holding tank. (see footnotes *1 and *3)

(*1) This “Permit” is not the same as the Ralls County Planning and Zoning “Wastewater Permit”.  Contact Mike Huff about a Planning and Zoning permit and requirements – see below for address and telephone number.  Permit fees are waived for upgrades and repairs.

(*2) The Health Department will assist with the application, if desired, and will arrange a visit to evaluate the site.  Specifications and suggestions for the systems and components that would meet minimum requirements will be provided for conventional treatment systems.  For non-conventional systems, submit plans designed and stamped by a Missouri Registered Engineer.  Examples: LPP, Drip Irrigation, etc.

(*3) If authorized to backfill and the system is covered before components are inspected, the installer will be required to provide written and signed certification that the system was constructed to comply with the approved permit application plans and/or applicable standards and regulations.  If notification is not provided, the system will not be approved and the installer may be required to uncover the system for inspection.

Planning & Zoning                                              911 Address                                                                         Ralls Co. Health  Dept.

Rev. 12/15

# Text boxes

Mike Huff, Administrative Office

57422 Parkview Trail

New London, MO 63459

(573)-985-5431 (home) (3679) office

Kathy Meyer

405 W. 1st, PO Box 434

New London, MO 63459

573-985-7121

17630 Hwy 19 Box 454

New London, MO 63459

(573) 985-3009